## Slide 1: Reliable and Real-time Communication in Industrial Wireless Mesh Networks
Presentation by Chaitanya VAdrevu
Song Han, Xiuming Zhu, Aloysius K. Mok, Deji Chen, Mark Nixon
RTAS 2011

## Slide 2: Motivation
Industrial wireless networks are deployed in harsh conditions
Devices may be mobile, wireless signal strengths may vary. So network topology will change
Reliability, real-time performance are very important as missing/delayed data may degrade performance
WirelessHART standard doesn’t specify how to meet these goals
The paper presents reliable counterparts of three routing graphs, algorithms for constructing them and scheduling them

## Slide 3: WirelessHART
Field devices
Access points
Industry standard protocol for wireless communication
Extension of HART (Highway addressable remote transducer) protocol
Centralized network management
Mesh network
Uses IEEE 802.15.4 in physical layer (which is also used in ZigBee, MiWi, etc)
Elements in WirelessHART network
  Wireless Field Devices: Data collection devices
  Gateway: Connects host applications with field devices
  Access Point: Connects field devices and Gateway
Host application
Host application
G
AP
AP
1
2
3
4

## Slide 4: Broadcast graph
Original Network
Broadcast graph
Graph connecting gateway to all devices
Used to broadcast common configuration, control messages to all nodes
Broadcast graph is reliable if there are at least two parents for every device in graph

## Slide 5: Uplink graph
Graph connecting all devices to gateway
Used to propagate devices’ data periodically to gateway
Uplink graph is reliable if every device has at least two in-edges
Original Network
Broadcast graph

## Slide 6: Downlink graphs
One per device
Used to send unicast messages from gateway to each device
Downlink graph to a node is reliable if
  There is one source and one sink
  Every intermediate node at least two in-edges
  There is only one cycle of length 2 and each node on cycle is parent of the node
Original Network
Downlink graphs for 3, 4

## Slide 7: Construction of reliable broadcast graph
Node is reliable if in-edge degree >=2
Goals of reliable broadcast graph
  Maximize number of reliable nodes
  Minimize average no. of hops from gateway to each node
Algorithm
  Add gateway, access points to set of explored nodes
  Select reliable nodes from remaining nodes
  For each of these nodes, sort in-edges in ascending order of average no. of hops to gateway
  Calculate no. of hops with first two edges
  Add node with minimum no. of hops to explored nodes
  If there are no reliable nodes at step 2, select node with maximum out-edges to explored nodes
  Goto 2
Complexity O(|V|3)
Reliable uplink graph is constructed in same way after reversing all edges

## Slide 8: Downlink graph
In WirelessHART standard, there is one reliable downlink graph from gateway to every node
This results in high configuration overhead as each downlink graph has to go from gateway through all intermediate nodes to the destination node
In Scalable reliable downlink routing (SRDR), each node contains a small local graph
Reliable downlink graph for each node can be obtained by assembling intermediate nodes’ local graphs
To support SRDR, WirelessHART is extended

## Slide 9: Constructing reliable downlink routes
Routes for gateway, access points are already known, and so are added to “nodes with known routes” list
Constraints when constructing routes for node v
  C1: v has at least two parents u1, u2, and they form a cycle
  C2: u1 is u2’s parent in u2’s local downlink graph
  C3: u2 has at least one parent from the cycle in Gu1
For each node, calculate average hops for every edge pair and select edge pairs satisfying C1 and (C2 or C3) with minimum average hops.
If C1 ^ C2 is satisfied, downlink route of v is R(v) = R(u2) -> g(v)
If C1 ^ C3 is satisfied, downlink route of v is R(v) = R(u1) -> g(v)
If constraints are not satisfied, a node with two parents from known list with minimum average latency is selected
u1
u2
v
u1
u2
a
b
u1
u2
v
C1
C2
C3

## Slide 10: SRDR - Optimized
In basic SRDR, routing is strictly according to ordered graph list
But when each node can keep graph information to multiple destinations, closest node can be chosen for routing
When packet arrives at a node, instead of using earliest graph ID, ordered graph list is searched backward and first graph ID that is stored in its routing table is selected
If this routing is successful, at the next node, all graph IDs up to current ID are removed

## Slide 11: Device/link failure recovery
WirelessHART has network maintenance commands which can be used to notify Network Manager of communication statistics, signal strengths, path/routing failure
Recovery includes finding nodes which are still reliable after network topology change and constructing network graphs again
Broadcast graph and Uplink graph can be easily constructed starting from the set of reliable nodes
Construction of downlink graph is more difficult

## Slide 12: Communication schedule, channel management
Devices specify bandwidth requirements, Network Manager allocates timeslots
WirelessHART constraints
  16 maximum concurrent active channels
  Each device can only be scheduled to transmit/receive in one time slot
  Simultaneous transmissions are allowed in shared timeslot
  On multi-hop path, early hops must be scheduled first
  Practical sample rates are 2n sec (-2 <= n <= 9)

## Slide 13: Constructing communication schedule
Timeslots are allocated in Fastest Sample Rate First policy (FSRF)
Algorithm:
For all nodes from fastest sample rates to slowest
  Schedule primary and retry links for publishing data
  Schedule primary and retry links for control data
  If link assignment is not successful, defer bandwidth request for that node
Primary links are exclusive but retry links are shared
Link for publishing/control data from a node A to node B is scheduled by allocating intermediate links on path from A to B one by one in depth-first manner
When there are 2 successors to a node, allocating time-slots for both successors is wasteful as only one is used. So, transmission rate to each of the successors is reduced to half of sample rate and data is sent on both. It is ensured that communication pattern is same as that of original sample rate.

## Slide 14: Performance
Communication overhead is low (less than 2 links per node)
Reachable nodes count between that of Broadcast tree and Max-reliable Broadcast graph in case of link failures
Recovery overhead to regain connectivity and reliability are worse than RDG(standard)
Configuration overhead for downlink graphs is much better than RDG(standard) and is comparable to single shortest path
By dividing traffic on successors,
  Scheduling success (no. of successfully scheduled nodes) is vastly improved
  For lower sampling rates, network utilization is much better

## Slide 17: Critical analysis
When SRDR – OPT is used, during routing, a node may forward data to another node skipping some nodes in the ordered graph list. But the other node may not be ready for receiving at that time slot. This problem is not discussed in the paper.
Since traffic is divided between two successors of a node, if any of them goes down, shouldn’t the communication schedule should be recalculated?

## Slide 18: References
Han, Zhu, Chen, Mok, Nixon, “Reliable and Real-time Communication in Industrial Wireless Mesh Networks” (RTAS 2011)
Han, Zhu, Chen, Mok, Nixon, “Reliable and Real-time Communication in Industrial Wireless Mesh Networks”, Technical Report (http://apps.cs.utexas.edu/tech_reports/reports/tr/TR-1994.pdf)
http://en.hartcomm.org/